## Slide 1: Wastewater treatment: current approaches and prospects for sustainable solutions
CEE6580

## Slide 2: Learning Objectives, Wastewater treatment and Waste-to-Energy
Recognize the various embedded energy in domestic wastewater (heat, nutrients, and organic carbon) and that most of the COD, and nutrients come from excreta (urine and feces)
Describe the elements of a functioning centralized sanitation system (User Interface, conveyance, centralized treatment system, disposal and/or reuse of treatment products)
Recognize sanitation options that don’t rely on centralized treatment (e.g. composting toilets, urine diverting dehydrating toilets, septic systems, constructed wetlands, biogas reactors)
Sketch out a typical US wastewater treatment plant and recognize the two greatest electricity demands (aeration of activated sludge and pumps to move wastewater)
Recognize the key benefits of of anaerobic digestion of wastewater organic matter to “biogas” (sludge reduction, production of useable biofuel, opportunity for co-digestion of wastewater organics with local food industry wastes (e.g. brewery wastes, food scraps, manure, cheese and yogurt whey)
Describe the overall biological conversions and key microorganisms for the following emerging/advanced biological treatment reactors
  UASBs, EBPR, Anammox, GSBR, MEC/MFC, Anaerobic membrane bioreactors (MBRs), algal ponds
Describe the following chemical treatment to recover nutrients from wastewater
  Struvite precipitation and ammonia stripping

## Slide 3: Upcoming…
Exam is scheduled for 4/17. Will cover learning objectives up through Wastewater treatment and Waste-to-energy
Final Project: be deciding on your topic over break
  Can be done individually or in groups up to 3 people
  Final presentation will be 8-10 minutes per person
  Must include reference to at least 4 publications (papers/chapters/reports) per person.
  Presentations will be held in class May 1, 3 & 8.

## Slide 4: Sustainable Sanitation and Water Management
www.sswm.org – run by EAWAG In Switzerland
Excellent technical resources and educational materials
We will explore website esp the pages on Water/nutrient cycles:
  https://sswm.info/perspective/water-nutrient-cycle-perspective

## Slide 5: Suggestions for session today:
Start a word or powerpoint document (or googledoc,etc).
Copy and paste images of websites screenshots as you go today.

## Slide 6: What is Water Used For?
Agricultural
Irrigation
Livestock farming
Industrial
Production of goods and energy
Transportation of goods
Process water
Domestic
Drinking water
Food preparation
Sanitation
Personal hygiene
Cultural asset
Gardening, Car wash
ECOSYSTEM
HUMAN USE
Plants
Animals
Photosynthesis
Soils
Aquatic Systems

## Slide 8: Nutrients
Nutrients are chemicals that all organism need to live and grow.
95 – 98% of living matter consists of C, H, O (MAHENDRAPPA 2007)
Although only needed in small amounts, macro- and micro- nutrients are essential for plant growth, blooming, photosynthesis, etc.
In relation to water manage- ment and sanitation, N and P are of high priority because of their high potential to cause eutrophication.
Macronutrients
Nitrogen (N)
Phosphorus (P)
Potassium (K)
Sulphur (S)
Magnesium (Mg)
Calcium (Ca)
Nutrients
Micronutrients
Various others
Non-mineral
Carbon (C)
Hydrogen (H)
Oxygen (O)
Adapted from: R. GENSCH (2010)

## Slide 9: Peak Phosphorus?!
http://www.sswm.info/sites/default/files/toolbox/CORDELL%20et%20al%202009%20Sources%20of%20Phosphorus%20Fertilisers_large.jpg

## Slide 10: There are three main reasons that lead to today’s situation of unsustainable management of water and nutrients:
Sectoral thinking
Unsustainable conventional approaches
Linear approaches to water and nutrient management

## Slide 11: So, let’s link the water cycle, the nutrient cycle and sanitation AND ENERGY…
Water
Sanitation
Agriculture
… and solve three (four) big problems in one go!
Source: Own Graph
Energy
Energy

## Slide 12
*Based on an average for a toilet that uses about 8 L of Water per flush (11).
With conventional waterborne flush-toilets, we mix
roughly 50 kg of faecal matter (per person/year)
roughly 500 l of urine (per person/year)
with roughly 20’000l of clean flushwater*
50 kg
500 L
20’000 L
If this wastewater is discharged untreated into rivers, an even higher amount of water is polluted!
http://thomasmayerarchive.de
(2) Unsustainable current approaches: Mixing what shouldn’t be mixed..
What is going wrong?
Notes: 12
This is a figure based on the Swiss average, for a toilet that uses about 8 L of Water per flush. However, toilets (mainly in North America) can use up to 5 Gallons (roughly 23l) just for one flush! This would add up to a water use (just for flushing!!) of almost 50’000 l per person and year – and the fact that the polluting substances make up just 1 % of the total wastewater!

## Slide 13: What products are we dealing with?
Greywater: wastewater from kitchen, bath, shower.
Yellow-water:
separated urine
Blackwater: urine, faeces & flush
Faecal sludge: solids and liquids accumulating in sanitation systems
A sanitation system must manage all products generated !
Excreta: urine & faeces
Introduction
Notes: Key messages
Households produce different waste products.
A sanitation system must deal with all products generated.
Next slide: What are the characteristics of waste products?
Additional information & questions:
The generation of liquid waste from human activities is unavoidable. However, not all humans produce the same amount of liquid waste. The type and amount of liquid waste produced in households is influenced by behaviour, lifestyle and standard of living of the population as well as by the governing technical and juridical framework. (Henze and Ledin 2001, pp. 57-72)
The following section describes the different liquid waste fractions produced by the households. Industrial wastewater is not included, although it makes up an important fraction of wastewater in some environments. (Tilley 2007, pp. 2)
Blackwater is the mixture of urine, faeces and flushing water, along with anal cleansing water (if anal cleansing is practiced) or dry cleansing material (e.g. toilet paper).
Greywater is used water which results from bathing, hand-washing, cooking or clothes-washing. It is sometimes mixed with, or treated along with, other types of products
Urine is urine that is not mixed with any faeces or water.
Faeces refers to (semi) solid excrement without any urine or water.
Excreta is the mixture of urine and faeces that is not mixed with any flushing water (although small amounts of anal cleansing water may be included).
Faecal Sludge is the general term for the undigested, or partially digested slurry or solid that results from the storage or treatment of blackwater or excreta.
Why distinguish between so many products?

## Slide 14: Characteristics of waste products
 | Total | Greywater*** | Urine | Faeces
Volume [l/cap·yr] | 25’000-100’000 | 25’000-100’000 | 500 | 50
Nutrients Nitrogen | 2 - 4 kg/cap·yr | 5% | 85% | 10%
Phosphorous | 0.3 - 0.8 kg/cap·yr | 10%** | 60% | 30%
Potassium | 1.4 - 2.0 kg/cap·yr | 34% | 54% | 12%
COD (organic material) | 30kg/cap·yr | 41% | 12% | 47%
Faecal coliforms | - | 104-106 /100ml | 0* | 107-109 /100ml
* healthy people
** can be as high as 50%, depending on washing and dish-washing powder used
*** values representative for industrialized countries
Introduction
Notes: Key messages:
Greywater, urine and faeces have distinct characteristics.
When dealing with waste products, it is important to account for their value and potential risks.
Next slide: Characteristics of waste products in words
Additional information & questions (also on next slide!):
Urine: Contains almost all the nitrogen and large parts of the potassium and phosphorous excreted by humans. N:P:K = 10:1:2 Urine is usually sterile (exceptions known by urinary tract infections).
Faeces: Mainly undigested organic matter made up of carbon. Faeces contain almost all pathogens:
bacteria (e.g. faecal coliforms, vibro cholerae)
viruses (e.g. rota virus)
protozoa (e.g. amoeba hystolitica)
helminths (e.g. Ascaris eggs)
Low nutrient content, but good characteristics as soil conditioner
Greywater:
Greywater is defined as household wastewater without input of human excreta
It includes used water from baths, showers, hand basins, washing machines, dishwashers, laundries and kitchen sinks
Big quantities with relatively low nutrient contents.
Big reuse potential:
Irrigation: Agriculture, landscape, aquaculture
Municipal uses: Fire protection, street cleaning, car washing, cooling, road construction operation, ...
Non-potable domestic uses: Toilet flushing, laundry, floor cleaning
Main issue: Toxic substances (organic compounds, metals, chlorine etc.), fats from kitchen, can affect natural treatment and disposal systems
Which constituents cannot be removed from waste products by most treatment technologies? How can that problem be solved?
Why is the volume an important parameter for describing waste products?
Are the nutrients in faeces readily available?

## Slide 15: Characteristics of waste products
 | Greywater | Urine | Faeces
Chemical contamination | Fats, oils and toxic substances org. compounds, chlorides, metals | Micro-contaminants e.g. hormons & antibiotics | Micro-contaminants e.g. Heavy metals
Biological contamination | Pathogens bacterias, viruses, helminths, protozoa | Almost sterile i.e. cross-contamination from feaces | Pathogens bacterias, viruses, helminths, protozoa
Value | Reuse potential for irrigation or municipal and non-potable domestic use | Nutrients (N, K and P etc.) => ideal fertilizer | Good soil conditioner, but only little nutrients
Introduction
Notes: Key message:
When dealing with waste products, it is important to account for their value and potential risks.
Next slide: What are the processes of sanitation systems?
Additional information & questions:
Potential reuse applications could be:
Greywater should be reused for irrigation, washing, etc.
Urine is a perfect fertilizer
Faeces are very good soil conditioner (after treatment)
=> The sanitation products are valuable!
Which constituents cannot be removed from waste products by most treatment technologies? How can that problem be solved?
Why is the volume an important parameter for describing waste products?
Are the nutrients in faeces readily available?
How can eutrophication of a lake be reversed?
How can future generations meet their phosphorus demand?

## Slide 16: Sanitation: What are the Functional Groups through which the products flow?
User Interface
e.g. Dry Toilet or Pour Flush Toilet
Collection
and Storage/ Treatment
e.g. Septic
Tank
(Semi-)
Centralised
Treatment
e.g. Anaerobic
Baffled Reactor
or Waste Stabilisation
Pond
Conveyance
e.g. Simplified
Sewer or
Tank Lorries
Use
and/or Disposal
e.g. Composting
or Leaching Field
Input products
safe & valuable output products
Systems and Technologies
Technologies which perform the same, or similar function, are grouped into „Functional Groups“
Notes: Key messages:
A sanitation system is a combination of technologies through which the products flow.
Technologies which perform the same, or similar function, are grouped into „Functional Groups“
Next slide: How can the Functional Groups be linked?
Additional information & questions:
User interface describes the type of toilet, pedestal, pan or urinal the user comes in contact with. User interface also determines the final composition of the product, as it is the place where water is introduced in the system. Thus, the choice of user interface is often dependent on the availability of water.
Collection and storage/treatment describes the ways of collecting and storing products generated at the user interface; storage often also performs some level of treatment.
Conveyance describes the way in which products are moved from one process to another. Although products may need to be moved in various ways to reach the required process, the longest and most important gap lies between on-site storage and (semi-) centralised treatment. For the sake of simplicity, conveyance is thus limited to moving products at this point.
(Semi-) centralised treatment refers to the treatment systems which, unlike those used on-site, are larger, require a greater inflow (that can usually not be met by just one family) and often more skilled operation.
Reuse and disposal refers to the ways in which products are ultimately returned to the soil, either as harmless substances or useful resources. Furthermore, products can also be re-introduced into the system as new products. A typical example is the use of partially treated greywater used for toilet flushing.
Which processes are not required in certain sanitation systems?

## Slide 17: Which technologies can perform which function?
Dry Toilet
Urine Diverting Dry Toilet
Urinal
Pour-Flush Toilet
Flush Toilet
Urine Diverting Flush Toilet
Single Pit
Single VIP
Dehydration Vaults
Septic Tank
Composting Chamber
Anaerobic Baffled Reactor
Anaerobic Filter
etc.
Human-Powered Emptying and Transport
Motorized Emptying and Transport
Simplified Sewers
Small-Bore Sewer
Conventional Gravity Sewer
Jerry Can/Tank
etc.
Anaerobic Baffled Reactor
Anaerobic Filter
Upflow Anaerobic Sludge Blanket
Trickling Filter
Waste Stabilisation Ponds
Activated Sludge
Constructed Wetland
Co-composting
etc.
Application of Urine
Application of Dehydr. Faeces
Compost
Irrigation
Aquaculture
Soak Pit
Leach Field
Land Application
Surface Disposal
etc.
User Interface
Collection
and Storage/ Treatment
Conveyance
(Semi-)
Centralised
Treatment
Use and/or
Disposal
Only selected combinations of technologies will lead to functional systems.
Systems and Technologies
Notes: Key messages:
Only selected combinations of technologies will lead to functional systems.
The most site-specific system option has to be selected on a case-to-case basis.
Note: in some systems, not all processes are required. Eg. When composting faeces locally, no conveyance nor central treatment is required.
Next slide: How can sanitation systems be classified?
Additional information & questions:
A system is a set of technologies, each processing the products until they are ultimately disposed of. In other words, processing all the waste products “from cradle to grave” should be considered. As aforementioned, one can distinguish between eight mainly different treatment systems whose technologies can be logically linked to form an effective system.
Though the system templates (i.e. groups of processes and products) are predefined, the exact system and favoured technology still have to be selected from among the options provided. The choice is context-specific and should be made on the basis of the local environment, culture and resources. Despite the different technology options available, a comprehensive study of the specific situation is necessary prior to making the final decision.
Who should choose the technology options and based on what criteria?

## Slide 18: Which technologies can perform which function?
Dry Toilet
Urine Diverting Dry Toilet
Urinal
Pour-Flush Toilet
Flush Toilet
Urine Diverting Flush Toilet
Single Pit
Single VIP
Dehydration Vaults
Septic Tank
Composting Chamber
Anaerobic Baffled Reactor
Anaerobic Filter
etc.
Human-Powered Emptying and Transport
Motorized Emptying and Transport
Simplified Sewers
Small-Bore Sewer
Conventional Gravity Sewer
Jerry Can/Tank
etc.
Anaerobic Baffled Reactor
Anaerobic Filter
Upflow Anaerobic Sludge Blanket
Trickling Filter
Waste Stabilisation Ponds
Activated Sludge
Constructed Wetland
Co-composting
etc.
Application of Urine
Application of Dehydr. Faeces
Compost
Irrigation
Aquaculture
Soak Pit
Leach Field
Land Application
Surface Disposal
etc.
User Interface
Collection
and Storage/ Treatment
Conveyance
(Semi-)
Centralised
Treatment
Use and/or
Disposal
Only selected combinations of technologies will lead to functional systems.
Systems and Technologies
Notes: Key messages:
Only selected combinations of technologies will lead to functional systems.
The most site-specific system option has to be selected on a case-to-case basis.
Note: in some systems, not all processes are required. Eg. When composting faeces locally, no conveyance nor central treatment is required.
Next slide: How can sanitation systems be classified?
Additional information & questions:
A system is a set of technologies, each processing the products until they are ultimately disposed of. In other words, processing all the waste products “from cradle to grave” should be considered. As aforementioned, one can distinguish between eight mainly different treatment systems whose technologies can be logically linked to form an effective system.
Though the system templates (i.e. groups of processes and products) are predefined, the exact system and favoured technology still have to be selected from among the options provided. The choice is context-specific and should be made on the basis of the local environment, culture and resources. Despite the different technology options available, a comprehensive study of the specific situation is necessary prior to making the final decision.
Who should choose the technology options and based on what criteria?

## Slide 19: Methanogenesis in Anaer. Digesters

## Slide 21: Current approaches in US: Example High-Tech Wastewater Treatment Plants
Which will need:
Long sewer network & pumps to get the wastewater to the plant
Electricity for aeration, pumps and other moving parts
Skilled (and thus expensive) operation & maintenance staff
High cost
Recycling difficult due to contamination of heavy metals, etc..
 Who will pay for this?

## Slide 22: Typical WW Trtmt Plant in the US (consumes average of 0.54kWhr/1000 L treated)
Anaerobic Digester
Biosolids (to landfills, currently)
Ithaca Area WWTP:
-6 million gallons of sewage per day.
-Tertiary treatment for P
Burns methane to provide 55% of plant Energy needs (electric and heat)
Biogas (CH4 and CO2)

## Slide 23
Basic mass flows and processes in typical US WWTF
Sewage
(raw WW)
Aeration tank
Settling
Anaer. Digester
Settling
Treated water
Polishing
Solids
Biogas
Sludges
air
CO2
Average electricity usage (wide range):
0.54 kWhr/cubic meter wastewater
(WW treatment is ~1-4 % of US electricity use

## Slide 24
Notes: Negative Effects? Human vs Ecological Health effects

## Slide 26
From McCarty, P.L., Bae, J., Kim, J., 2011. Domestic Wastewater Treatment as a Net Energy Producer–Can This be Achieved? Environmental Science & Technology 45, 7100–7106. https://doi.org/10.1021/es2014264

## Slide 27
From McCarty, P.L., Bae, J., Kim, J., 2011. Domestic Wastewater Treatment as a Net Energy Producer–Can This be Achieved? Environmental Science & Technology 45, 7100–7106. https://doi.org/10.1021/es2014264

## Slide 28: Status Quo (left) vs Vision (right) for US WWTFs (current proposal idea we are working on w/WW plant Ithaca)

## Slide 29: Emerging Biotech for sustainable WW treatment
Anaerobic (or aerobic/anaerobic cycling) treatment
  E.g. UASB, Anaerobic Membrane bioreactors
  Granular SBRs
  Anammox
Nutrient (N & P) removal/recovery
  EBPR
  Algal ponds
  Chemical : ammonia stripping; Struvite (MgNH4PO4) precipitation

## Slide 30: UASB

## Slide 31: Granules

## Slide 32: Membrane bioreactors
Membranes replace the need for a settling tank after a bioreactor
Can be used with either aerobic or anaerobic processes

## Slide 33: Anaerobic Membrane Bioreactor configurations

## Slide 34: Major concerns with membranes
Energy costs (pressure to send water through)
Fouling

## Slide 35: Nutrients N & P

## Slide 36: Nitrogen removal strategies
Nitrification/Denitrification
  NH3 + 2O2 = NO3- + H+ + H2O
  NO3- + (5 e- + 6H+ )= ½ N2 +3 H2O
Partial nitrification/Anammox (= nitritation/anammox)
  ½ NH3 + ¾ O2 = ½ NO2- + ½ H+ + ½ H2O
  ½ NH3 + ½NO2- + ½ H+= ½ N2 + H2O

## Slide 37
Reminder of the nitrogen cycle!
Notes: Most of the nitrogen on earth is in the gaseous form, in N2
We’re going to start by focusing over here on nitrogen fixation. Very important because organisms need a useable form of nitrogen…

## Slide 38: Nitrification/denitrification
Nitrification: aerobic process in which bacteria oxidize reduced forms of nitrogen
Denitrification: anaerobic process by which oxidized forms of nitrogen are reduced to gaseous forms, which can then escape into the atmosphere
Why is it important to remove these forms of nitrogen?
Notes: This is important because the release of nitrogen to the aquatic environment can also cause eutrophication.
Denitrifiers play several roles — some positive, some negative — in wastewater
treatment processes. We exploit the activities of denitrifiers in biological
processes designed to remove nitrate from municipal or agricultural wastewaters.
On the other hand, if unwanted denitrification occurs in the bottom of settling
tanks, the resulting nitrogen gas bubbles can cause rising sludge problems (the
bubbles essentially lift floc particles off the bottom of the tank, lowering the
solids-separation efficiency). The key to preventing rising sludge problems is to
minimize the concentration of degradable carbon entering the settling tank and/or
minimize the residence time of solids in the sludge blanket at the bottom of the
tank. discharged into the environment, it can deplete the natural oxygen resources. Eutrophication is the process by which bodies of water become rich in mineral and organic nutrients causing plant life, especially algae, to proliferate, then die and decompose thereby reducing the dissolved oxygen content and often killing off other organisms. Wastewater treatment in the plants involve primary, secondary and tertiary treatment. Primary treatment deals with removing large solids while secondary treatment removes the smaller solids and tertiary treatment involves the disinfection of the wastewater through chemical means.

## Slide 39
Both breathe oxygen

## Slide 40
Nitrococcus

## Slide 41
Denitrifiers (for instance Pseudomonas) then reduce nitrate to N2

## Slide 42: Nitrogen removal strategies
Nitrification/Denitrification
  NH3 + 2O2 = NO3- + H+ + H2O
  NO3- + (5 e- + 6H+ )= ½ N2 +3 H2O
Partial nitrification/Anammox (= nitritation/anammox)
  ½ NH3 + ¾ O2 = ½ NO2- + ½ H+ + ½ H2O
  ½ NH3 + ½NO2- + ½ H+= ½ N2 + H2O

## Slide 43: Nitritation/Anammox

## Slide 44: Phosphorus removal also very important!
Preventing eutrophication (for instance can cause algal blooms)
Recovery/reuse
  Global phosphorus reserves are limited
  Large amounts lost in human, agricultural, industrial wastes
Notes: remains is of lower grade and more
difficult to access than ever before
Excessive inorganic phosphate (Pi) supply to freshwater negatively
affects water quality and ecosystem balance through a process known
as eutrophication1. Limitations on allowable Pi discharges from
municipal and industrial sources through wastewater treatment have
proven effective in reducing Pi levels in many waterways2. Increasingly
stringent Pi limits for effluent wastewater are expected in the future
and hence efficient and reliable Pi removal methods are required.
Because of the massive quantity of wastewater treated daily (more
than 120 billion liters in the US alone3), any improvement in existing
methods should have tangible economic and ecological consequences.

## Slide 45: Enhanced biological phosphorus removal (EBPR)
Produces effluent containing low levels of phosphorus
  Enables concentration of phosphorus 10-50X
Relies on a specific group of bacteria, collectively called polyphosphate accumulating organisms (PAOs)
  Phosphorus stored by PAOs as intracellular granules of polyphosphate
  For use, polyphosphates can be solubilized or sludge can be applied directly
Notes: to take up phosphate
from wastewater in excess of their growth requirements,
under alternating anaerobic and aerobic/anoxic conditions
enables concentration of phosphorus
by 10– 50 times. The process produces a solids stream
(called sludge in wastewater literature) that is rich in
phosphorus. This stream contains phosphorus at 5– 7%
[13 ], and is suitable for phosphorus recovery.

## Slide 46
EBPR requires alternating anaerobic and aerobic conditions
Three intracellular polymers are central to the PAO metabolism
PAOs have growth advantage in anaerobic conditions due to ability to hydrolyze polyphosphate
Under aerobic conditions, PHAs stored anaerobically are oxidized to produce energy
Amount of phosphate taken up exceeds that released
PHA=
polyhydroxyalkanoate
Current Opinion in Biotechnology 2012, 23:878–883
Notes: The hydrolysis of polyphosphate enables PAOs to gain
energy under anaerobic conditions, which is used to take
up organic carbon, primarily short-chain volatile fatty
acids (VFAs) [12]. This unique metabolism provides
PAOs advantages over most other organisms, which are
unable to use carbon sources anaerobically. The reducing
equivalents for the conversion of VFAs to PHAs is primarily
provided by the hydrolysis of glycogen, although the
oxidation of VFAs through the full or partial tricarboxylic
acid (TCA) cycle could also supply part of the reducing
equivalents, particularly when glycogen is limiting [18].
Under the subsequent aerobic conditions, PHAs stored
anaerobically are oxidized to produce energy for phosphate
uptake, glycogen replenishment and cell growth
[12]. Because the amount of phosphate taken up by PAOs
is in excess of that released anaerobically, a net accumulation
of phosphorus in biomass is achieved. Some PAOs
have been found to be able to use nitrate and nitrite in
place of oxygen as the electron acceptor for PHA oxidation

## Slide 47: Who are the PAOs?
‘Candidatus Accumulibacter phosphatis’ (Accumulibacter) seems to be a dominant organism
Gram-positive Tetrasphaera-related organisms (Actinobacteria) also regarded as PAOs
  Metabolic processes poorly understood, appear to differ from those of Accumulibacter
**No PAOs have been isolated in pure culture
Notes: *stress that neither isolated so not very well understood.
The most well known group of PAOs is ‘Candidatus
Accumulibacter phosphatis’ (Accumulibacter). It belongs
to subclass 2 of Betaproteobacteria and is closely related to
Rhodocyclus [21]. Pure cultures of Accumulibacter are still
not available despite numerous attempts to isolate these
organisms. However, they have been frequently enriched
in laboratory-scale EBPR reactors [12], and have also
been found to be abundant in full-scale EBPR sludges
typically representing 5–20% of the bacterial community

## Slide 48
Fluorescence in situ hybridization (FISH) of a floc from an EBPR reactor. Accumulibacter specific probe in blue
Notes: A FISH image of a floc from a lab-scale EBPR reactor and 400X magnification. The image was captured using a Zeiss LSM 510 confocal microscope with two channels: FITC and Cy5. The EUBmix probe (FITC) was used to stain all bacteria, which appear in green. The PAOmix probe (Cy5) was used to stain Candidatus Accumulibacter Phosphatis, which appear in blue

## Slide 49: Fertilizer from Urine (or anaerobic Digester supernatant)
Struvite (ammonium magnesium phosphate) is a phosphate mineral with formula: NH4MgPO4·6H2O.

## Slide 50: Nutrient (N & P) recovery from source- separated urine
Yellow-water:
separated urine
From: Water 2013, 5(3), doi:10.3390/w5031262

## Slide 51: Granular Sequencing Batch Reactor (GSBR)
anaerobic
aerobic
settle
Fill/mix
drain

## Slide 52: Granules
Enhanced Bio P Removal also occurs in these reactors (anaer/aero cycling)

## Slide 53: Algal ponds: for nutrient removal & algae production

## Slide 54: Constructed wetland types for wastewater/graywater treatment
Microbial conversions in SF wetlands
Surface Flow
SF
Sub-surface Horizontal Flow
SSF

## Slide 55: What about in the Global South??

## Slide 56: Which technologies/approaches??
Dry Toilet
Urine Diverting Dry Toilet
Urinal
Pour-Flush Toilet
Flush Toilet
Urine Diverting Flush Toilet
Single Pit
Single VIP
Dehydration Vaults
Septic Tank
Composting Chamber
Anaerobic Baffled Reactor
Anaerobic Filter
etc.
Human-Powered Emptying and Transport
Motorized Emptying and Transport
Simplified Sewers
Small-Bore Sewer
Conventional Gravity Sewer
Jerry Can/Tank
etc.
Anaerobic Baffled Reactor
Anaerobic Filter
Upflow Anaerobic Sludge Blanket
Trickling Filter
Waste Stabilisation Ponds
Activated Sludge
Constructed Wetland
Co-composting
etc.
Application of Urine
Application of Dehydr. Faeces
Compost
Irrigation
Aquaculture
Soak Pit
Leach Field
Land Application
Surface Disposal
etc.
User Interface
Collection
and Storage/ Treatment
Conveyance
(Semi-)
Centralised
Treatment
Use and/or
Disposal
Only selected combinations of technologies will lead to functional systems.
Systems and Technologies
Notes: Key messages:
Only selected combinations of technologies will lead to functional systems.
The most site-specific system option has to be selected on a case-to-case basis.
Note: in some systems, not all processes are required. Eg. When composting faeces locally, no conveyance nor central treatment is required.
Next slide: How can sanitation systems be classified?
Additional information & questions:
A system is a set of technologies, each processing the products until they are ultimately disposed of. In other words, processing all the waste products “from cradle to grave” should be considered. As aforementioned, one can distinguish between eight mainly different treatment systems whose technologies can be logically linked to form an effective system.
Though the system templates (i.e. groups of processes and products) are predefined, the exact system and favoured technology still have to be selected from among the options provided. The choice is context-specific and should be made on the basis of the local environment, culture and resources. Despite the different technology options available, a comprehensive study of the specific situation is necessary prior to making the final decision.
Who should choose the technology options and based on what criteria?

## Slide 57: SSWM.info section on water-nutrient cycle perspective
https://sswm.info/perspective/water-nutrient-cycle-perspective

## Slide 58: Sanitation crises worldwide
1 Billion people lack access to safe drinking water
3.6 Billion people lack access to sanitation for excreta
High capital and energy costs of industrialized waste treatment are prohibitive in non-industrialized locales
UN’s Millenium Development Goals’ call for

## Slide 59: Objectives of Sustainable Sanitation
Health and hygiene
  Effective barrier between user and environment
  Prevention of exposure to excreta at all levels of the sanitation process
Environment and natural resources
  Protection of natural resources
  Recycling, low energy consumption, low emissions
Technology and operation
  Adaptation to local circumstances
  Robustness against floods, power cuts, water shortages, etc.
Financial & economic issues: Consideration of total (lifecycle) costs
Socio-cultural & institutional aspects: Acceptance by the community

## Slide 60: Conventional Forms of Wastewater Management and Sanitation
- Retention of solids
- Infiltration of liquids
Dry (pit) systems (on-site)
Waterborne systems (centralised)
Source: http://i.bnet.com/blogs/toilet.png [Accessed: 30.01.2012]

## Slide 61: Sustainable Sanitation is a simple Approach
  The essential principles
    Wastewater and excreta should not be considered as a waste, but as valuable resources.
    Sanitation systems should be organised in a socially acceptable and economically viable manner.
  There is no “one-fits-all” approach, much rather, the most adequate solution has to be found from case to case, considering climate and water availability, agricultural practices, socio-cultural preferences, affordability, safety, and technical prerequisites, etc.

## Slide 62: Promising technologies for international sanitation
Key features:
  Decentralized (small scale) so communities take ownership/benefit
  Low energy costs (ideally no Electricity-reliance)
  Low water usage
  Ideally, value added product (e.g fertilizer, natural beauty)

## Slide 63: E.g. The Challenge for Small Islands in Indonesia
Fresh water is very limited
Coral reefs sensitive to waste
Agriculture: only bananas?
Energy: all imported (kerosene; electricity)
Most of population: use beaches as toilet

## Slide 64: Example System: Waterless system with urine diversion
Faeces
Urine Diverting Dry Toilet & Urinal
Double Dehydration Vaults
Human Powered Emptying and Transport
Application of Treated Faeces to Crops
Application of Urine
To Crops
Storage Tank
Jerry Can / Tank
Greywater
Greywater Treatment
Urine
(Semi-) Centralised Treatment
User Interface
Collection and Storage/ Treatment
Conveyance
Use and/or Disposal
Systems and Technologies
Irrigation of Crops
Notes: Key message/Figure:
Flow scheme illustrating waste processing in a dry sanitation system with urine separation and final application of all products.
Next slide: 2nd Example: Water-based alternating double pit
Additional information & questions:
The user interface(s) in this system generate(s) two different products: faeces and urine. Thus, each product must be treated separately with its own appropriate technologies and processes.
Faeces are stored in a double dehydration vault where they dehydrate. In the absence of moisture, organisms cannot grow and, thus, smells are minimised and pathogens destroyed. By using two vaults, the faeces are allowed to dehydrate and become sanitised, while allowing the system to remain in use.
Urine can either be collected in a bucket for later discharge on the ground or a garden, or it is stored in a tank for future transport. It is generally accepted that if urine is stored for at least one month, it will be safe for agricultural reuse.
Since a sanitation system must deal with all the generated waste products, an adequate reuse solution must also be found for greywater – an often forgotten resource. Greywater should not be added to the double dehydration vault where the faeces are being dried, nor should it be added to urine. In most cases, it is conveyed by drains or sewers and finally treated centrally, although many technologies exist for the beneficial use of greywater at the household level.
For both urine and faeces there is no technology option required at the ‘Treatment’ process step: the arrows indicate that after ‘Conveyance’, ‘Reuse and Disposal’ is the next process step required.
In this system, the different processing steps do not offer any technology choices. If the Compendium user does not like the technology options associated with this system, he/she should select a different system, since it is not possible to substitute or rearrange the technology options in a given system.
FOOTNOTE: Although greywater management is an essential part of sanitation, this Compendium is primarily concerned with systems and technologies related directly to excreta. For a more comprehensive summary of dedicated greywater technologies we refer you to the following resource: Morel A., Diener S. (2006). Greywater Management in Low and Middle-Income Countries, Review of different treatment systems for households or neighbourhoods. Swiss Federal Institute of Aquatic Science and Technology (Eawag). Duebendorf, Switzerland.

## Slide 65: Distributed systems for Excreta or blackwater
Compost it:
(Aerobic treatment)
Digest to biogas:
(Anaerobic treatment)

## Slide 66: Composting toilets

## Slide 67: Learning Objectives, Wastewater treatment and Waste-to-Energy
Recognize the various embedded energy in domestic wastewater (heat, nutrients, and organic carbon) and that most of the COD, and nutrients come from excreta (urine and feces)
Describe the elements of a functioning centralized sanitation system (User Interface, conveyance, centralized treatment system, disposal and/or reuse of treatment products)
Recognize sanitation options that don’t rely on centralized treatment (e.g. composting toilets, urine diverting dehydrating toilets, septic systems, constructed wetlands, biogas reactors)
Sketch out a typical US wastewater treatment plant and recognize the two greatest electricity demands (aeration of activated sludge and pumps to move wastewater)
Recognize the key benefits of of anaerobic digestion of wastewater organic matter to “biogas” (sludge reduction, production of useable biofuel, opportunity for co-digestion of wastewater organics with local food industry wastes (e.g. brewery wastes, food scraps, manure, cheese and yogurt whey)
Describe the overall biological conversions and key microorganisms for the following emerging/advanced biological treatment reactors
  UASBs, EBPR, Anammox, GSBR, MEC/MFC, Anaerobic membrane bioreactors (MBRs), algal ponds
Describe the following chemical treatment to recover nutrients from wastewater
  Struvite precipitation and ammonia stripping